## Slide 1: Graph Cuts for Skull Stripping
Ahsan Mahmood

## Slide 2: Binary Segmentation

## Slide 3: Graph Cuts

## Slide 4: Graph Cuts

## Slide 5: Maxflow
The max-flow min-cut theorem states that in a flow network, the maximum amount of flow passing from the source to the sink is equal to the total weight of the edges in the minimum cut
Cut: Edges which if removed would disconnect the source from the sink

## Slide 6: Maxflow

## Slide 7: Data
T1 weighted MRI Images from assignment in BME 775
Sagittal sections
Corpus Callosum clearly visible

## Slide 8: Data
Background noise
Used hard threshold to remove it
Some non-brain anatomical structures visible

## Slide 9: Building Graph
Each pixel assigned a corresponding node
Each edge between pixels assigned a flow capacity
Created virtual source and sink
Source forward connected to pixels
Pixels forward connected to sink

## Slide 10: Pixel – Pixel Weights
High if belong to the same class (target or background)
  Low otherwise
How to determine if in same class?
  Gradients!
Very likely to be in the same class if gradient directions parallel
Weighting function

## Slide 11: Source/Sink – Pixel Weights
Source -> Pixel : high if background class
Pixel -> Sink: high if target class
How to tell if target or background?
  Seeds!
What does “high” even mean?
  I don’t know

## Slide 12: Generating Seeds
Usually seeds added via user interaction
Automation would be nice
Use a heuristic inspired by thresholding and quantiles
Main Idea: Skull generally appears brighter than white matter
Get all pixels that fall within one standard deviation of the class mean

## Slide 13: Generating Seeds
Used 98th percentile as a threshold for skull
Intensities between 50th and 70th percentile worked well for “white matter” class
Skull Seeds
“WM” Seeds

## Slide 14: Strict Cutoff
Target is skull
Source -> Pixel: Only connected to background
  If pixel intensity < target mean
Pixel -> Sink : Only connected if pixel is in target class
  If pixel intensity > target mean
Weights to connected pixels: Intensities of the pixels
Not connected means edge weight is set to zero

## Slide 15: Strict Cutoff
Background Nodes
Foreground Nodes

## Slide 16: Intensity Difference
Flow capacities should vary on a range
As the difference from the target class mean intensities change, so should the corresponding weights to source/sink.
Source/Sink connected to all pixels
Edge weights: Intensities weighted by squared difference from class mean
  Other decays tended to over/undershoot
Background Class: Skull
Target Class: White Matter

## Slide 17: Intensity Difference
Background Nodes
Foreground Nodes

## Slide 18: Hybrid Approach
Combines cutoffs based on classes and intensity differences
Source is only connected to background pixels (pixels lying outside the brain) and the skull seeds
  The weights on these edges are set to the maximum flow value
Conversely the sink is only connected to non-background pixels
  The weights for edges connecting white matter seeds are set to maximum
  Other non-skull regions are weighed according to intensity differences from the white matter class mean

## Slide 19: Intensity Difference
Background Nodes
Foreground Nodes

## Slide 20: Pruning
An final optimization
Lots of background pixels (very low intensity)
  Have high pixel-pixel weights
  Algorithm wants to push flow through them and not the skull
Solution: DESTROY them
Remove pixel – pixel edges that are solely between very low intensity pixels

## Slide 21: Pruning - Hybrid
After Pruning

## Slide 22: Pruning – Intensity Difference
After Pruning

## Slide 23: Final Mask
Combined result from hybrid and intensity difference

## Slide 24: Some Additional Examples

## Slide 25: Conclusion
Not a straightforward graph cut problem
  No clear boundary edges
Lingering issues
  Noise
  Smoothness
  That pesky corpus callosum
Adding an explicit distance metric will prevent unlikely cut and act as a smoothness term
Postprocessing steps like morphological dilation and erosion could solve issues with holes